Seventh Framework Programme 
Theme 9 Space FP7-SPA.2009.1.1.02

Monitoring of climate change issues (extending core service activities)

Grant agreement for:	Collaborative Project (generic).

Project acronym: 	MONARCH-A

Project title: 	MONitoring and Assessing Regional Climate change in High latitudes and the Arctic

Grant agreement no.	242446

Start date of project: 	01.03.10

Duration: 	36 months

Project coordinator: 	Nansen Environmental and Remote Sensing Center, Bergen, Norway

D1.1.2: Global (North of 50°N latitude) monthly and 5-day fields of Snow Depth

Due date of deliverable: 31.08.2011

Actual submission date: 09.09.2011

Organization name of lead contractor for this deliverable: CNRS

Authors:  Anne-Lise J. Dhomps, Nelly M. Mognard and Alexei V. Kouraev

| Project co-funded by the European Commission within the Seventh Framework Programme, Theme 6 Environment |
| --- |
| Dissemination Level |
| PU | Public | X |
| PP | Restricted to other programme participants (including the Commission) |  |
| RE | Restricted to a group specified by the consortium (including the Commission) |  |
| CO | Confidential, only for members of the consortium (including the Commission) |  |

| ISSUE | DATE | CHANGE RECORDS | AUTHOR |
| --- | --- | --- | --- |
| 01 | 07/09/2011 | Report | A.-L. Dhomps |

SUMMARY

The aim of this paper is to provide a description of monthly and 5-days fields of Snow Depth provided as deliverables 1.1.2. This dataset is a contribution to the Work Package 1.1 "The decadal snow dynamics and their consequences for GHGs and climate". Snow depths are calculated with satellite brightness temperature, ground temperature and surface air temperature. Brightness temperatures come from the passive microwave SSM/I (Special Sensor Microwave/Imager) on board the DMSP. Ground temperatures are from ISBA and surface air temperature from NCEP reanalysis. Monthly and 5-days fields of Snow Depth are available from 1988 to 2010.

MONARCH-A CONSORTIUM

| Participant no. | Participant organisation name | Short name | Country |
| --- | --- | --- | --- |
| 1 (Coordinator) | Nansen Environmental and Remote Sensing Center | NERSC | NO |
| 2 | The University of Sheffield | USFD | UK |
| 3 | Universität Hamburg | UHAM | NO |
| 4 | Centre National de la Recherche Scientifique | CNRS | FR |
| 5 | Scientific foundation Nansen International Environmental and Remote Sensing Center | NIERSC | RU |
| 6 | Universitetet i Bergen | UiB | NO |
| 7 | Danmarks Tekniske Universitet | DTU | DK |
| 8 | Institut Francais de Recherche pour l'Exploitation de la Mer | IFREMER | FR |

No part of this work may be reproduced or used in any form or by any means (graphic, electronic, or mechanical including photocopying, recording, taping, or information storage and retrieval systems) without the written permission of the copyright owner(s) in accordance with the terms of the MONARCH-A Consortium Agreement (EC Grant Agreement 242446).

All rights reserved.

This document may change without notice.

# Table of Contents

Table of Contents	5

1	Introduction	6

2	Sources data	7

2.1	Brigthness Temperature	7

2.2	Air Temperature	7

2.3	Ground Temperature	7

3	Datasets	8

3.1	Equations	8

3.2	Calculated datasets	8

3.3	Deliverables	9

4	Snow depth maps	10

5	References	11

List of Figures

Figure 1: Few Snow Depth pentads from October the 18th to June the 24th in 2008.	10

Figure 2: Snow Depth winter monthly fields in 2008	11

Figure 3: Snow Depth spring monthly fields in 2008	12

List of Tables

Table 1: List of pentads	9

# Introduction

The aim of this paper is to provide a description of monthly and 5-days fields of Snow Depth (SD) provided as deliverables 1.1.2. This data are a contribution to the Work Package 1.1 "The decadal snow dynamics and their consequences for GHGs and climate".

SD are “observed” fields. They are calculated with satellite brightness temperature, ground temperature and surface air temperature.

# Sources data

## Brigthness Temperature

We have used passive microwave data set from the SSM/I (Special Sensor Microwave/Imager) instrument onboard the DMSP (Defense Meteorological Satellite Program) series (since 1987). These radiometers with incidence angle from 50.2 to 52.8 degrees provided measurements of brightness temperature at different frequencies and at different (vertical or horizontal) polarizations. We have used the data from the 19 GHz and 37 GHz channels at horizontal polarization. The National Snow and Ice Data Center (NSIDC, www.nsidc.org) provides the SSM/I data mapped to the Equal Area (625 km² resolution) SSM/I Earth Grid (EASE-Grid) projection. An overview of the EASE-Grid projection can be found at the http://nsidc.org/data/ease/, and more detailed information at the http://nsidc.org/data/ease/ease grid.html. We have used data in the global projection (EASE-ML grid), that has 1383 pixels in longitude, and 586 values in latitude. Corresponding latitude and longitude for this EASE-Grid are provided by NSIDC.

In order to perform the processing only on land, we used a mask provide by NSIDC. To minimize the effects of ice and snow melting, only night brightness temperatures were used (thus affecting the choice of ascending or descending passes).

The initial data were averaged to obtain the 73 pentad (5 days) mean values in order to get continuous spatial coverage.

## Air Temperature

For the air temperature, the National Center for Environmental Prediction (NCEP) daily global reanalysis has been used. They are available on http://www.esrl.noaa.gov/psd/cgibin/dbsearch/-DBSearch.pl?Dataset=NCEP+Reanalysis+Daily+Averages+Surface+Level&Variable=Air+Temperature&group=0&submit=Search. Daily fields are available and they are on a 2.5° regular grid.

The NCEP air temperatures have been interpolated to the EASE-Grid and averaged into pentads.

## Ground Temperature

To estimate the temperature at the base of the snowpack, the ground temperature simulated by the Interaction between the Soil-Biosphere-Atmosphere (ISBA) LSS are used (Boone et al. [2006]). Daily 1° temperatures fields have been interpolated to the EASE-Grid and averaged to create climatology of 73 pentads fields over the 1983-1994 period.

# Datasets

## Equations

SD are calculated as describe in Biancamaria et al. [2008]. It results from the combinaison of a dynamic algorithm (Mognard & Josberger, [2002] and Josberger & Mognard, [2002]) and a static Algorithm developed by Chang et al. (1987). The dynamic algorithm is defined with:

TGI is the Thermal Gradient Index which represent the effect of the bulk temperature gradient through the snowpack,

Tg is the Ground temperature,

Ta is the Air Surface Temperature.

SG is the Spectral Gradient as defined by Josberger and Mognard [2002].

SD is the snow depth,

 is the slope of the linear relation between SG and TGI determined with ETAC multiyear average (Foster and Davy [1988]).

## Calculated datasets

SD have been calculated for all pentads (1 to 73) from 1988 to 2010. Pentads are calculated in hydrological years: pentad 1 of 1988 starts at the end of September 1987. Monthly fields have also been calculated over the entire period. They are on the EASE-ML Grid, and above 50°N.

Table 1: List of pentads

We observed some gaps during the first years of the period, mostly on North America. They have to be investigated further. Gaps are also present in 1994 and 1995. According to NSIDC, during 1994, substantial amounts of swath data over Alaska and the Canadian Prairies are missing beginning early in 1994 until May 1995. During this period, the data tape recorder on the DMSP-F11 failed. As a result, it was necessary to download data to ground stations more frequently than usual. Data download and acquisition could not occur simultaneously, consequently data gaps exist in the EASE-Grid data for Alaska and the Canadian Prairies from early 1994 until data acquisition by the DMSP-F13 SSM/I began in May 1995.

## Deliverables

SD are in little endian binary files. Format is integer on 16 bits, and array of 1383 lines by 70 rows and unit is millimeter. Non-defined values (no brightness temperature) are set to -1.

Snow Depth (SD) file names are:

sd average monthmm yyyy.bin

sd boreal yyyy ppp.bin

with mm=month, yyyy=year and ppp=pentad.

NSIDC mask is in file Ml loci land50 coast0km.1383x586.bin. Latitude and longitude for EASE-Grid are provided by NSIDC in files MLLATLSB MLLONLSB respectively.

# Snow depth maps

Figure 1: Few Snow Depth pentads from October the 18th to June the 24th in 2008.

We can observe the raise of the snow depth between the 18th of October 2007 (pentad 05) to the 26th of January 2008 (pentad 25), and then the thawing from the 16th of March (pentad 35) to the 24th of June (pentad 55). January is the most snow-covered month. We can observe some geographic influence in snow depth with more than 50 cm of snow in Quebec and West of the Rocky Mountains for North America, and in the Eastern Eurasia, the Central Russian Plateau and in Kamchatka for Eurasia. Contrary, in the North-West Canadian Territories, the Ob river basin and the Lena river basin show small content in snow with value lower than 10 cm.

Figure 2: Snow Depth winter monthly fields in 2008

Figure 3: Snow Depth spring monthly fields in 2008

Month fields illustrated the snow accumulation and melting as much as the pentads showed above. It would be interesting to study inter-annual variability.

# References

Biancamaria, S., N. Mognard, A. Boone, M. Grippa, A. Josberger, 2008, “A satellite snow multi-year average derived from SSM/I for the high latitude regions”, Remote Sensing of Environment, vol. 112, 2447-2568.

Boone, A., N. Mognard, B. Decharme, H. Douville, M. Grippa, K. Kerrigan, 2006, “The impact of simulated soil temperatures on the estimation of snow depth over Siberia from SSM/I compared to a multi-model climatology”, Remote Sensing of Environment ,vol. 101, 482-494.

Chang, A. T. C., J. L. Foster, D. K. Hall, 1987, “Nimbus-7 SMMR derived global snow cover parameters”, Annals of Glaciology, 9, 39-44.

Foster, D.J. and R.D. Davy, 1988, “Global Snow Depth Multi-Year Average”, USAFETAC/TN-88/006. Illinois: Scott Air Force Base. 48 pp.

Grippa, M., N. Mognard, T. Le Toan, E.G Josberger, 2004, “Siberia snow depth climatology derived from SSM/I data using a combined dynamic and static algorithm”, Remote Sensing of Environment, vol. 93, 30-41.

Josberger, E.G. and N. Mognard, 2002, “A passive microwave snow depth algorithm with a proxy for snow metamorphism”, Hydrological Processes, vol. 16, 15557-1586. doi:10.1002/hyp.1020.

Mognard, N. and E.G. Josberger, 2002, “Northern Great Plains 1996/97 seasonal evolution of snowpack parameters from satellite passive-microwave measurements”, Annals of Glaciology, vol. 34, 15-23.

END OF DOCUMENT